## Slide 1: Accessibility
Identify the vulnerable populations to consider
Discuss requirements for accessibility and other special needs

## Slide 2: Historic Fire
L’Isle Verte

## Slide 3: Mobility Impairments
Must accommodate everyone
All occupants not intimate with fire shall be kept safe

## Slide 4: IBC Chapter 10
Four or more floors
  Elevator
No exit access stairs
Stairs 48” between handrails
  Normal with sprinklers
Area of refuge

## Slide 5: IBC Chapter 11
Not all areas
  Work areas where change in elevation is essential
  No elevators
Not all routes
  One
  Site plan
  60 % of entrances
General circulation

## Slide 6: IBC Chapter 11
Parking spaces
Hospital sleeping rooms
Hotel rooms
Apartments
Assembly seating areas
Self-service storage
Bathrooms
Check-out aisles
Recreation facilities

## Slide 7: International Codes
https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/441786/BR_PDF_AD_M2_2015.pdf

## Slide 8: Vulnerable Populations
Movement impaired
Visually impaired
Hearing impaired
Cognitive disability
Elderly
Children
Large groups
Isolation
Unfamiliar
Asleep
Intoxicated
Non-Native speakers
Committed to task
Situationally disabled
Compounded effects

## Slide 9: Code Requirements
Combination horn/strobe
520 Hz smoke alarms
Voice alarms?
Area of refuge
Occupant evacuation elevators
Assistive listening systems
Stair markings?
Signage

## Slide 10: Future
Increased occupant evacuation elevators
Stairway descent devices
Multi sensorial wayfinding
Personalized emergency messaging
?